## Slide 1: Discussion on Idea of Efficient RL with LLM Integration for Power Grid Control
Presenter : Shoaib Ahmad

## Slide 2: Challenges in Modern Power Grid Control
Safety (Cascading failures)
Economics (generation, losses, redispatch)
Complexity (Lack of Realtime Decisions)
Traditional Methods:
• Rule-based systems → inflexible
• Pure optimization → too slow for real-time control

## Slide 3: EffiRL : System Architecture Overview
Layer | Component | Purpose | Input | Output | Result Achieved
1. Environment | Grid2Op Simulator | Power grid physics | Actions | States, Rewards | Realistic power flow simulation
2. Reward System | Multi-objective function | Guide agent behavior | Grid state | Scalar reward | Balances safety + economics + survival
3. Observation | State representation | What agent sees | Grid2Op obs | Vector (288-dim) | Line flows, voltages, costs
4. Action Space | Discrete actions | What agent can do | Policy output | Grid2Op action | Topology + dispatch + storage
5. Policy Network | Actor-Critic NN | Decision making | Observation | Action probabilities | Learns optimal control
6. Training Algorithm | PPO | Learn from experience | Episodes | Updated policy | Converges to safe operation
7. LLM Integration | Gemini API | Domain knowledge | Grid state text | Action suggestions | Guides exploration

## Slide 4: EffiRL Framework: RL + LLM Synergy
Three Control Strategies Compared:
Pure PPO (Baseline RL) – learns by trial and error
Pure LLM Control – Gemini directly operates the grid (no learning)
PPO + LLM Priors (Proposed) – LLM guides RL during training

## Slide 5: Training Process Breakdown
Phase | Episode Range | What Happens | Policy Behavior | Reward Trend | Result
Random Exploration | 0-500 | Agent explores randomly | 10-20% good actions | -10 to 5 | Learning from failures
Initial Learning | 500-1500 | Finds basic patterns | 30-40% good actions | 5 to 10 | Avoids obvious failures
Rapid Improvement | 1500-3000 | Discovers strategies | 50-70% good actions | 10 to 15 | Success rate increases
Fine-Tuning | 3000-5000 | Optimizes details | 80-90% good actions | 15 to 18 | Near-optimal behavior
Convergence | 5000+ | Stable performance | 90-95% good actions | 18 ± 2 | Converged policy

## Slide 6: Multi-Objective Reward and Simulation
Component | Formula | Range | Weight | Purpose | Result Achieved
Survival | R_survive = +1 per timestep | [0, 1] | α=1.0 | Stay alive | 100% success rate
Overload | R_overload = 1 - 2·(Σ violations / max) | [-1, 1] | β=0.5 | Safety | 0% overloads
Cost | R_cost = -(losses + redispatch)·price | [-1, 0] | η=0.5 | Economics | 12% cost reduction
Total | R = α·R_s + β·R_o + η·R_c | [-1.5, 2.0] | Weighted sum | Balance objectives | 18.5 avg reward
Note : For IEEE 5-Bus Output Data seems to be satisfactory but that will not be the case in real environment.

## Slide 7: Performance Comparison of Approaches
Metric | Target | Pure PPO | Pure LLM | PPO-Prior | Achievement
Success Rate | >95% | 100% ✅ | 65% ❌ | 100% ✅ | Exceeded target
Avg Reward | >15 | 16.8 ✅ | 10.5 ❌ | 18.5 ✅ | 23% above target
Stability (σ) | <3.0 | 2.1 ✅ | 4.2 ❌ | 1.8 ✅ | Most stable
Training Speed | Minimize | 5000 eps | N/A | 3000 eps ✅ | 40% faster
Key Insights:
• PPO + LLM Priors → 40% faster training
• Combines learning & domain knowledge
• Best performance and stability

## Slide 8: Summary of EffiRL Findings
Result | What It Proves | Significance | Future Impact
100% Success Rate | RL can reliably control power grids | Safety-critical deployment viable | Industry adoption possible
40% Faster Training | LLM priors accelerate learning | Reduced training costs | Practical for large systems
18.5 Avg Reward | Multi-objective optimization works | Balances competing goals | Better than single-objective
0% Overloads | Safety constraints learned | No line failures | Meets grid codes

## Slide 9: Research Motivation
Current Gap | Our Opportunity | Expected Impact
Limited Scale Testing | We have 177-bus real data | First large-scale EffiRL validation
Toy Problem Validation | Real power system topology | Industry-relevant results
Research Question
"Can LLM-guided reinforcement learning scale from educational benchmarks (5-bus) to real-world power systems (177-bus) while maintaining safety and efficiency?"

## Slide 10: Dataset Comparison - What We're Scaling
Characteristic | Proven: IEEE 5-Bus | Proposed: 177-Bus Real System | Scaling Factor
Network Size | 5 buses | 178 buses | 35.6x larger 📈
Transmission Lines | 8 lines | 176 lines | 22x more complex 📈
Load Points | 11 loads | 66 loads | 6x more demand 📈
Control Complexity | 48 discrete actions | ~800 actions (est.) | 16.7x harder 📈
State Space | 288 dimensions | ~2000 dimensions (est.) | 6.9x richer 📈

## Slide 11: Key Finding from Prior Work
LLM priors accelerate RL training by 40% without sacrificing performance
Multi-objective optimization balances safety + economics successfully
System achieves 100% success rate with zero line overloads
Metric | Pure PPO | Pure LLM | PPO + LLM | Proven Benefit
Success Rate | 100% | 65% | 100% | Safe control ✅
Training Speed | 5,000 episodes | N/A | 3,000 episodes | 40% faster ✅
Performance | 16.8 reward | 10.5 reward | 18.5 reward | 10% better ✅
Stability | σ = 2.1 | σ = 4.2 | σ = 1.8 | Most stable ✅

## Slide 12: What We Have vs What We Need
Component | Status | Current | Required
Topology | ✅ Complete | 178 buses, 176 lines | ✅ Have it
Line Parameters | ✅ Complete | R, X, B values | ✅ Have it
Load Data | ⚠️ Verify | 1.24 MW total | Clarify scale
Generators | ❌ Insufficient | Only 1 generator | 3-5 generators
Thermal Limits | ❌ Missing | None | MVA ratings for 176 lines
Time-Series | ❌ Missing | Static snapshot | 24-hour profiles
Blockers: Generator data and thermal limits must be added before training

## Slide 13: Novel Aspects
Contribution | Novelty | Significance
Scalability Validation | First EffiRL on 177-bus | Proves method scales 35x
Real-World Data | Actual power system | Beyond toy problems
LLM Scaling Analysis | Does LLM help more at scale? | New insight
Deployment Framework | Real-time integration | Industry relevant
Benchmarks | Large-scale RL metrics | Reference for field

## Slide 14: What We Will Answer
Research Question | Method | Expected Answer
Q1: Does EffiRL scale to real grids? | Train on 177-bus | ??
Q2: Do LLM priors help MORE at scale? | Compare speedup (5-bus vs 177-bus) | ??
Q3: Can it handle real-time loads? | Time-series testing | Yes, if data available
Q4: What's the computational cost? | Measure training time | 100-120 hours (maybe more on CPU)
Q5: How does it compare to baselines? | Benchmark vs OPF/MPC | Competitive or better

## Slide 15: Thank you
Brita Tamm
502-555-0152
brita@firstupconsultants.com
www.firstupconsultants.com